## Slide 1
Solar Energy Production in Urban Environments
Integration of Balcony Power Plant into the OBLO Smart Home System
Ognjen Stojisavljević | Marija Antić
RT-RK Institute for Computer Based Systems | Faculty of Technical Sciences, University of Novi Sad
Smart Home
Photovoltaics
IoT
Solar Energy
Notes: Good afternoon, my name is Ognjen Stojisavljević, I work as a researcher at RT-RK Institute in Novi Sad, and this paper was prepared together with my colleague Marija Antić.
The question we started from is simple: if you live in an apartment and you cannot put panels on the roof, what can you do?
What we built is a balcony power plant connected to a smart home system, so you can see exactly how much energy your balcony is producing at any moment.
I will take about fifteen minutes, and I am happy to take your questions at the end.

## Slide 2
Problem Statement & Motivation
Rising Energy Costs
Electricity prices in the EU have increased significantly. Households seek ways to reduce dependency on the public grid.
Urban Housing Constraints
The majority of urban residents live in apartment buildings where traditional rooftop PV installations are not feasible.
Sustainability Pressure
Growing environmental awareness and decarbonization goals drive demand for accessible, small-scale renewable solutions.
💡 Solution: Balcony PV systems + IoT smart home integration → accessible, monitorable, low-cost solar for apartments
Notes: Electricity prices across Europe have been rising, and people are looking for ways to reduce their bills — but most of them live in apartments where rooftop solar is simply not an option.
Balcony power plants solve the access problem — they plug into a standard socket, require no permits in most European countries, and can be installed in under an hour.
But we wanted to go one step further — instead of just generating energy and hoping for the best, we connected the system to a smart home platform so the user can actually see what is happening.
That combination of local energy production and real-time awareness is the core of this paper.

## Slide 3
Related Work
Balcony PV Systems
1. Krauter & Bendfeld (2024): efficiency ranking of PV microinverters; yield estimations for balcony power plants 2. Polański (2025): applicability in large-panel prefabricated urban housing 3. Fakhraian et al. (2021): urban rooftop PV potential 4. Brito et al. (2016): small-scale distributed generation in residential buildings
Smart Home & IoT Energy
1. Badar & Anvari-Moghaddam (2020): comprehensive review of smart home energy management systems 2. Ivanović et al. (2019): data acquisition and storage in smart home solutions 3. Nikolić et al. (2025): cloud-enabled smart home energy optimization 4. IEA PVPS (2023): global trends in photovoltaic applications
Research Gap: Limited work combining real-time balcony PV monitoring with smart home infrastructure using real-world operational data
Notes: There is good existing work on balcony PV systems — Krauter and Bendfeld looked at microinverter efficiency, Polański studied large residential buildings — and separately there is strong work on smart home energy management from Badar, and from our own colleagues Ivanović and Nikolić at RT-RK.
What none of this work does is combine the two — there is no study that integrates a balcony PV system into a smart home platform and validates it with real operational data.
That is the gap we address.

## Slide 4
OBLO Smart Home Architecture
Controller (Gateway)
Central hub. Manages all peripheral devices. Supports IP, BLE, ZigBee, Z-Wave, Matter. Receives and processes PV production data.
Cloud Service
Enables remote access outside local network. Routes HTTP/MQTT between client app and controller. Stores per-device data with unique IDs.
Client Application
Mobile or web interface. Displays real-time power output, hourly/daily/monthly energy statistics. Supports local (MQTT) and remote (HTTP) modes.
Peripheral Devices
Sensors (data collection) and actuators (command execution). Balcony PV acts as an energy sensor — power (W) and cumulative energy (kWh).
Notes: The platform we integrated with is OBLO — a smart home system developed at RT-RK built around four components: a local controller, a cloud service, a client application, and peripheral devices.
The controller is the central piece — it manages all connected devices and supports a wide range of protocols, which is what made the integration straightforward.
From the platform's perspective, the balcony PV system is simply another peripheral device — a sensor that reports power and energy values, just like a temperature sensor reports temperature.

## Slide 5
Integration — Hardware Setup
PV Installation
2 solar panels: connected in parallel to one microinverter
Total capacity: 600 W peak (2 × 300 W panels)
Inverter comm.: proprietary 2.4 GHz RF protocol
No battery: all energy consumed or fed into household network
DTU (Data Transfer Unit)
MCU: ESP8266 (Wemos D1 mini)
RF module: NRF24L01+ 2.4 GHz
Firmware: Open-source OpenDTU project
Discovery: mDNS — no static IP needed
Interface: Embedded HTTP server, JSON REST API
Notes: The physical installation is two three-hundred-watt panels connected to a single microinverter — six hundred watts total, no battery storage.
The challenge is that the microinverter communicates over a proprietary two-point-four gigahertz RF protocol that cannot be read directly, so we needed a bridge.
We built that bridge using an ESP8266 microcontroller and an NRF24 radio module running the open-source OpenDTU firmware — the total hardware cost is under ten euros.
The result is that the inverter's proprietary RF output becomes a standard JSON REST API that any system can read over the local network.

## Slide 6
Integration — Data Flow & Software
1
RF Link
Microinverter → DTU (ESP8266)
Proprietary 2.4 GHz RF
2
REST API
DTU HTTP server returns JSON
AC voltage, current, power, energy
3
HTTP Polling
OBLO Controller polls DTU
Every 10 minutes via HTTP GET
4
Processing
Controller parses JSON
Maps to OBLO device properties
5
MQTT / Cloud
Data pushed to cloud & mobile app
Hourly / daily / monthly aggregation
Monitored Parameters: AC Voltage (V) · AC Current (A) · Total Energy Generated (kWh) · Instantaneous Power Output (W)
Notes: The data flow has five steps: the inverter transmits to the DTU over RF, the DTU exposes it via HTTP, the OBLO controller polls that endpoint every ten minutes, parses the response, and publishes the values via MQTT to the cloud and the mobile app.
The ten-minute polling interval was chosen deliberately — it is enough granularity for residential monitoring while adding negligible load to the network.
The important architectural point is that the controller treats the PV system as a virtual sensor — the rest of the platform has no idea it is dealing with a solar panel, which means the integration is clean and reusable.

## Slide 7
Testing Setup & Methodology
Period
September 2025 – February 2026 (6 months)
Location
Suhr, Switzerland · 47.37°N, 8.08°E · Temperate Central European climate
Climate
Annual irradiation: 1000–1400 kWh/m² · Significant seasonal variation · Low winter irradiation (Dec–Jan)
Data collection
Automatic via microinverter → DTU → OBLO controller → cloud DB · No manual intervention
Aggregation
Sampled at regular intervals → aggregated into hourly, daily, monthly statistics within OBLO cloud
Metrics evaluated
Total energy production · Financial savings · CO₂ reduction · Specific yield · Capacity factor
Notes: The system ran continuously from September 2025 to February 2026 — six months of real operational data from an installation in Suhr, Switzerland.
I want to be explicit upfront: this covers autumn and winter, not summer — so the numbers you are about to see are the low end of what this system can do.
Data collection was fully automated — the controller logged everything without any manual intervention, which is itself part of what we were validating.

## Slide 8
Results — Monthly Energy Production
Chart: 
| Sep 65.0 | Oct 42.0 | Nov 23.9 | Dec 12.2 | Jan 14.4 | Feb 21.1
Energy Production (kWh) | 65 | 42 | 23.9 | 12.2 | 14.4 | 21.1
178.6 kWh
6-month total
65 kWh
Peak (September)
12.2 kWh
Min (December)
5.4×
Sep vs Dec ratio
Notes: September was the strongest month at sixty-five kilowatt-hours, and from there production fell steadily through the autumn, reaching its lowest point in December at twelve-point-two kilowatt-hours.
That September-to-December ratio of five-point-four to one shows just how sensitive these systems are to the season.
From January onward production starts recovering — the days are getting longer — and critically, there were no gaps in the data across the entire six months.

## Slide 9
Results — Daily Production Profile (September)
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
Daily Production (kWh) | 2.1 | 2.8 | 3.3 | 3.5 | 3.2 | 2.9 | 1.4 | 0.9 | 2.7 | 3.4 | 3.2 | 3.1 | 2.6 | 2.2 | 3 | 3.3 | 2.8 | 2.5 | 1.8 | 2.1 | 2.4 | 3.1 | 3.4 | 3.2 | 2.9 | 1.2 | 0.6 | 1.8 | 2.2 | 2.7
Peak days: Up to ~3.5 kWh/day on sunny days
Poor days: < 1 kWh on overcast/cloudy days
~3.5 kWh
Best day (Sep)
< 0.5 kWh
Worst winter days
Weather
dominant factor
Notes: If we zoom into September day by day, you can see the weather signature clearly — the peaks are sunny days reaching about three-point-five kilowatt-hours, and every dip is an overcast day.
In winter, that same chart would show most days below half a kilowatt-hour.
This is the reason real-time monitoring matters — without visibility into what is actually being produced, the user has no way to act on it.

## Slide 10
Performance Metrics
Financial Savings
53.58 CHF
178.6 kWh × 0.30 CHF/kWh
Based on Swiss residential tariff (ElCom 2024)
CO₂ Emission Avoided
17.86 kg CO₂
178.6 kWh × 100 g CO₂/kWh
Swiss electricity mix emission factor (treeze 2021)
Specific Yield
298 kWh/kWp
178.6 kWh ÷ 0.6 kWp
Within expected range for balcony PV systems
Capacity Factor
6.8 %
178.6 ÷ 2628 kWh × 100%
Seasonal (autumn–winter); reflects day/night & weather
Notes: Over the six months, the system saved fifty-three-point-five-eight Swiss francs — at thirty cents per kilowatt-hour, which is the current Swiss residential tariff — and avoided seventeen-point-eight-six kilograms of CO₂.
The specific yield of two-ninety-eight kilowatt-hours per kilowatt-peak is consistent with what Krauter and Bendfeld report for comparable systems.
The capacity factor of six-point-eight percent looks low, but I want to be clear — this is a winter number. Annual capacity factors for these systems typically run between ten and fifteen percent.

## Slide 11
System Reliability & Operational Results
Zero Data Loss
No significant data gaps recorded during the entire 6-month monitoring period
Stable MQTT
Communication between inverter interface, controller, cloud, and mobile app ran without interruption
Negligible Latency
Delay from energy production measurement to app visualization was negligible for residential use
Seamless Integration
PV unit successfully abstracted as a virtual energy sensor within OBLO — transparent to rest of platform
Notes: Across six months of continuous operation, we recorded zero data loss — no communication failures, no gaps in the dataset.
The MQTT stack connecting the inverter interface, the controller, the cloud, and the mobile app remained stable throughout without a single interruption.
And because the PV unit is abstracted as a virtual sensor, adding a new energy device in the future — a heat pump, an EV charger — requires no changes to the platform at all.

## Slide 12
Discussion & Limitations
✓ Key Discussion Points
• Specific yield 298 kWh/kWp within expected literature range (Krauter & Bendfeld 2024) • Capacity factor 6.8% is seasonal — not representative of annual performance • Integration with OBLO adds monitoring value over standalone PV systems • Balcony systems are complementary to, not a replacement for, rooftop installations • Accessibility advantage: plug-in, no ownership of roof required, simple regulations
⚠ Limitations
• Single installation only — results may not generalize to all orientations/climates • Observation window: 6 months, autumn–winter. Summer performance not captured • Urban constraints: non-optimal panel orientation, potential shading from buildings • No battery storage — energy not used immediately is exported, not stored • Financial model assumes fixed tariff — real savings depend on consumption patterns
Notes: The results are consistent with the literature — the specific yield and capacity factor are both in the expected range for a balcony system running through autumn and winter.
The limitations are real and I want to name them directly: this is one installation, six months of data, and the financial calculation assumes a fixed tariff.
But the contribution I want to highlight is not the energy number itself — it is the demonstration that this integration works cleanly and can be replicated on any platform that speaks HTTP and MQTT.

## Slide 13
Conclusion & Future Work
Conclusions
1. Balcony PV systems can be seamlessly integrated as virtual energy sensors within an existing smart home platform 2. 178.6 kWh produced over 6 months → 53.58 CHF saved · 17.86 kg CO₂ avoided — measurable real-world impact 3. Specific yield (298 kWh/kWp) and capacity factor (6.8%) consistent with literature for autumn–winter conditions 4. IoT integration adds monitoring and awareness value beyond standalone PV installations 5. The architecture is scalable and replicable for other devices and deployments
Future Work
→ Extend monitoring: full annual and multi-year dataset → Production forecasting: use historical data + weather API → Smart automation: trigger appliances during peak solar output → Multi-installation study: different orientations, climates
Notes: To summarize: a six-hundred-watt balcony system produced one-seventy-eight-point-six kilowatt-hours over six months, saved fifty-three francs, and avoided eighteen kilograms of CO₂ — and it did all of this as a fully integrated part of a smart home platform.
The next steps we are most interested in are extending the dataset to cover a full year and building smart automation on top of the production data — so that household appliances can run automatically when solar output is at its peak.
With that, I am happy to take your questions.

## Slide 14
Thank You!
Questions & Discussion
Ognjen Stojisavljević | ognjen.stojisavljevic@rt-rk.com
RT-RK Institute for Computer Based Systems, Novi Sad, Serbia
Supported by the Ministry of Science, Technological Development and Innovation · Contract 451-03-34/2026-03/200156
Notes: Thank you for your attention — I would be happy to take your questions.
Q: Hardware cost? — The DTU costs under ten euros. Panels and inverter together range from one-fifty to three hundred euros.
Q: Why not a direct API from the inverter? — Proprietary RF protocol, not documented. OpenDTU reverse-engineered it — only open solution available.
Q: Summer performance? — Not in our dataset. Estimated six-hundred to eight-hundred kilowatt-hours per year for a six-hundred-watt system in Switzerland.
Q: Works on other platforms? — Yes. Standard REST and MQTT — not specific to OBLO.